## Slide 1
HYDRO 5
Mangrove Still Desalination System and
Saltwater Evaporation Greenhouse
System Description
HYDRO5 consists of a nature-inspired, low-cost desalination system. Seawater and brine from the existing desalination plant is treated in by the Mangrove still process to produce fresh water via evaporation and condensation and edible salt.
The desalination system is composed of a series of interconnected desalination panels where evaporation and condensation processes occur. The outputs of each unit are distilled water and brine. In addition, each unit can gather occasional rainwater falling on its external surface. Once the feed water is pumped into the tank, the hydraulic circuit works by gravity.
The distilled water produced by the panels, together with the rainwater, are collected and pumped to a cultivation greenhouse while the brine is pumped to a salt factory. In this unit salt is produced by evaporation and ventilation of the brine. The produced water is used to irrigate a greenhouse and produce tropical fruits.
Furthermore a Saltwater Evaporation Greenhouse (SEG) is developed. In this system the combination of evaporation and transpiration is intended to generate atmospheric moisture, which is converted into usable fresh water by means of condensation. In the greenhouse halophytes and mangroves are planted in order to optimize the evaporation. Fresh water will be used to improve productivity of the tropical fruits cultivation greenhouse.
Brine
Brine Tank
Mangrove Still System
Fresh water collection tank
Cultivation Greenhouse
Rainwater
Salt Factory
Concentrated Brine Tank
Water for irrigation
Saltwater Evaporation Greenhouse
Salt
Crop/plant species
Seawater
Seawater Tank
Brine well

## Slide 2
Technical Specifications
Mangrove Still System
Mangrove Area requirement = 0.23 m2/l of seawater treated/d
Seawater influent = 770 l/d
Expected Fresh water production = 200 l/d
Mangrove Still System Area = 162 m2
Yearly average = 3.3-3.7 l/m2 d
N° of Cascade-wick solar still panels = 76 units
Salt Factory
Area requirement = 30 m2
N° of salt production panels = 10 units
Expected salt production = 2 kg/d
Saltwater Evaporation Greenhouse (SEG)
Area Requirements = 30 m2
Pineapple Production = 145 kg/year
Papaya Production = 563 kg/year
Benefits
HYDRO 5 offers a low cost solution to the treatment of seawater and brine to recover salt and water
Production of sweet water from saltwater and/or brine
Production of salt
Operates a greenhouse to grow tropical fruits and thus decreases the need for importing tropical fruits