## Slide 1
HYDRO 3
Remote and innovative rainwater harvesting system
for irrigation
System Description
HYDRO3 consists of a low-cost, innovative rainwater harvesting system for remote areas, where house roofs are not available.
A shallow, subsurface water collection system is designed to collect rainwater by drainage, to transport it to storage tanks, and possibly to utilize water for agricultural irrigation. For instance, in Mykonos harvested water will be used to irrigate oregano which requires small amounts of water.
Online meteorological parameters e.g. rainfall, wind, humidity, pressure are monitored using a weather station in order to optimize the design of the system. Automated irrigation is performed using soil humidity sensors coupled to dripline irrigation systems.
Rainwater
Rainwater collection system
Rainwater storage tank 1
Rainwater storage tank 2
Water for irrigation
Crop/plant species

## Slide 2
Expected Results:
> 60 m3/year of harvested water
Expected production of oregano> 800 kg/year
Energy consumption <0.5 kWh/m3 of harvested water
0.4 ha irrigated area
Technical Specifications for Mykonos
Average annual rainfall = 319 mm
Subsurface rainwater collector of approximately 280 m2 and depth of 60cm.
Two flexible cylindrical tanks of structural grid with total cumulative capacity of 60m3
Total water harvesting capacity > 60 m3 / year
Automated system of drip irrigation in oregano crops of 4000m2
Benefits
Cheap water supply at remote areas without other water supply
Savings of freshwater
Create business case with little input
Minimization of construction and operation costs to create an economically viable and profitable water collection and irrigation system
Payback period < 3 years