## Slide 1
HYDRO 4
Rainwater harvesting and treatment system for the production of irrigation and potable water and for aquifer recharge
System Description
HYDRO4 is a rainwater harvesting system that can be applied to domestic residences to reclaim water for multiple purposes. Rainwater is collected and used for domestic non-potable uses. Part of the collected rainwater is treated by a slow sand filter (SSF) which is populated by microorganisms. The system is structured by layers of sand and gravel to enable different processes to purify the water for potable use.
Surface runoff is collected using a novel bioswale system, filtered and stored into the aquifer. The water will be used to cultivate 0.2 ha lavender. Lavender was chosen to produce high added value essential oil. Nutrients will be provided through composting of greens available on-site.
Rainwater
Rainwater storage tank
Slow Sand Filtration
Storage Tank
Drinking water
Water for Domestic non potable uses
Surface runoff
storage tank
Filtration
Aquifer Recharge
Water for irrigation
Rainwater Infiltration
Crop/Plant species
Essential Oil Distillation
Essential Oil

## Slide 2
Technical Specifications for Average Rainfall of 319 mm/year
Rainwater Collection Systems
Roof Rainwater Collection Area = 438 m2
Total Rainwater Harvesting Capacity = 126 m3/year
Surface Runoff Area = 350 m2
Total Surface Runoff Water Harvesting Capacity = 133 m3/year
Slow Sand Filter for Potable Water
Target filtration rate of 0.12 m/h
Filter Area = 0.2 m2
Flow rate of Potable Water after Installation: 0.4 L/min
Volume of Potable Water = 27 m3/year
Agricultural Production
Lavender Dried Floral Stems = 280 kg/year
Essential oil distillation = 3,3 l/year
Benefits
Decentralized solution to increase water supply in drought emergency situations
Water recovery for domestic non potable uses
Production of drinking water > 10 m³ /year
Aquifer recharge to store water and improve the ecological status of groundwater, 200 m³ of stored water/year
Fresh water recovered to irrigate 0.2 ha of crops, corresponding to 1000 kg/year lavender for essential oil production.